## Slide 1: mmSubArray: Enabling Joint Satellite and Terrestrial Networks in Millimeter-wave Bands
Rohith Reddy Vennam, Ish Kumar Jain, Nagarjun Bhat, Suriyaa M, Luke Wilson, Dinesh Bharadia

## Slide 2: Terrestrial networks (5G)
5G base station coverage area
We have more smart phones than people in the world (>8B), highlights the importance for connectivity and accessibility.
Terrestrial networks such 5G offers a high speed and low latency link to vast number of users.
User with active 5G connection
5G Base
station
5G link
High speed and low latency links

## Slide 3: Terrestrial networks: Coverage is limited
5G base station coverage area
No coverage area
User waiting for connection
Link failure
5G Base
station
Limited coverage
High speed and low latency links
Terrestrial networks’ coverage is limited to few km

## Slide 4: Satellite direct-to-device connectivity
5G base station coverage area
Satellite direct-to-device connectivity
5G Base
station
Satellite enabled coverage
Satellite
Ubiquitous coverage
Satellite direct-to-device link
With latest advancements in smartphones and LEO satellites, terrestrial devices can now directly connect to satellites
  Ex: Starlink direct-to-cell connectivity
Ref: starlink.com/business/direct-to-cell

## Slide 5: Satellite direct-to-device connectivity: challenges
5G base station coverage area
5G Base
station
Terrestrial operator
network
Satellite direct-to-device link
Long fiber backhaul
Not scalable
Long fiber backhaul to operator network
Ref: starlink.com/business/direct-to-cell
Satellite
Ubiquitous coverage
Ground station
The link between satellite and terrestrial operator network is the bottleneck due to the disjointness between both networks.
Satellite enabled coverage

## Slide 6: Proposed Joint satellite and terrestrial networks (JointNets)
5G base station coverage area
5G Base
station
Terrestrial operator
network
Satellite direct-to-device link
Avoid fiber backhaul and join satellite ground stations and 5G base stations
Satellite
Ubiquitous coverage
Ground station
Wireless backhaul
Scalable
Satellite enabled coverage
JointNets: High speed mmWave Backhaul link between satellite ground station and 5G base station

## Slide 7: Two requirements for JointNets
Ground station
Satellite
Direct to device
User within 5G coverage
5G Base
station
Remote user
5G base station coverage area
5G Link
Satellite Link
High speed wireless
mmWave backhaul
Enable Backhaul
Enable wireless backhaul and join satellite and terrestrial networks
Enable coexistence
Both networks should operate without affecting each other, even when they are nearby and using the same frequency bands.

## Slide 8: JointNets challenge: Interference
5G Link
High speed wireless
mmWave backhaul
Ground station
Satellite
Direct to device
Satellite
Uplink (desired)
Remote user
User within 5G coverage
5G Base
station
Ground station to satellite uplink transmission leakage towards 5G base station leading to co-channel interference
Satellite
Uplink leakage (undesired)
When a satellite ground station and a 5G base station are in proximity and use overlapping frequency bands, it can lead to interference issues
Ground stations transmit uplink signals in the 27.5-30 GHz band with high transmit power. Further, unlike GEO satellites, LEO satellites move rapidly, requiring frequent dish realignment and causing sidelobe leakage.
These can lead to significant interference at 5G base stations, resulting in poor signal-to-noise ratio (SNR) or link failures.
5G base station coverage area

## Slide 9: Interference: Co-channel and Adjacent channel
Co-channel Interference
  When multiple sources transmit in overlapping frequency bands.
  Interference power increases the noise floor, resulting in poor signal-to-noise ratio (SNR) or may cause link failure.
Adjacent channel interference
  When there is a simultaneous transmission in the adjacent channel.
  Adjacent channel interference increases dynamic range on the receiver, there by degrading step size and leading to increase in quantization noise.
Desired band/channel
Desired band/channel
Notes: Q)Are in-band and co-channel interference same?

## Slide 10: Current approaches to address interference (when nearby)
Approach | Full Spectrum Usage (Co-existence) | Coverage gaps (Coexistence) | Enabling backhaul | Comments
Frequency separation (Filtering) |  |  |  | Significant wastage of spectrum (full overlap can lead to 100% wastage)
Direction Separation (Beam nulling) |  |  |  | Effective spectrum usage but creates coverage gaps and cannot backhual
How to enable backhaul and coexistence
while fully utilizing spectrum and avoiding coverage gaps?

## Slide 11: Our approach: key insights
Frequency
Direction
Supporting users in the interference direction within the non-overlapping band using Phased Array-2
Serving users in non-interfering directions with overlapping band using phased array-1
Assumption
  Satellite ground station interference only occurs in partial bandwidth
Key insights
  Beam non-overlapping bands in interference-prone or any other necessary direction
  Beam overlapping bands into non-interfering directions.
Frequency
Overlapping band
Non-overlapping band
Notes: Requirements
  Full spectrum usage requires efficient usage of full bandwidth
  No coverage gaps mandates ability to serve users in all directions
Requirements
  ⟹ Full spectrum usage requires efficient usage of full bandwidth
  ⟹ No coverage gaps mandates ability to serve users in all directions

## Slide 12: Fundamental problem with phased array
Frequency
Phased array
  Beams full bandwidth in one direction
  It cannot split and beam in different directions
Notes: Requirements
  Full spectrum usage requires efficient usage of full bandwidth
  No coverage gaps mandates ability to serve users in all directions
Requirements
  ⟹ Full spectrum usage requires efficient usage of full bandwidth
  ⟹ No coverage gaps mandates ability to serve users in all directions

## Slide 13: Proposed mmSubArray solution
Ground station
Satellite
Direct to device
Satellite Link
Remote user
User within 5G coverage
5G base station coverage area
Non-overlapping band
High speed wireless
mmWave backhaul
mmSubArray approach
  Divide overall bandwidth into multiple overlapping and non overlapping bands
  Use different phased arrays for each
5G Link
5G Base
station
Hz
Overlapping band
Hz

## Slide 14: Proposed mmSubArray solution: Beaming non-overlapping band to satellite ground station
SDR
Gain
Phased Array
Phased Array
Gain
Ground station
mmSubArray
Frequency
Non-overlapping band
Enabling backhaul through non-overlapping band

## Slide 15: Proposed mmSubArray solution: Suppressing interference and supporting users
user
Beaming in non-interfering angles
Beaming nulling to suppress below noise floor
Frequency
Overlapping band
SDR
Gain
Phased Array
Phased Array
Gain
mmSubArray
Enabling coexistence by suppressing interference and effectively supporting users in non interfereing directions

## Slide 16: Simulator Results: Beamforming in frequency and space
Beamforming gain in space domain
Beamforming gain in frequency and space domain

## Slide 17: Simulator Results: Splitting and Nulling
Supporting user in interferer directions
Splitting: Supporting users in non-interferer directions
Splitting + Nulling: Supporting users in non-interferer directions with nulling

## Slide 18: Over-the-air experiments: Hardware Setup
Hardware setup with commercial phased arrays mimicking 5G user (UE), Interferer and Base station
Interferer
UE
5G Base Station
18

## Slide 19: Over-the-air experiments: Results
Adjacent channel Interference does not significantly affect the link performance
Suppressing interference below the noise floor enables coexistence in overlapping bands
Partial overlap (>25%) results in similar degradation as full bandwidth overlap
A non-overlapping band only experiences adjacent channel interference, which remains unaffected and helps in enabling backhaul

## Slide 20: mmSubArray Prototype: Demo video
mmSubArray suppresses interference in overlapping bands by beaming in non-interfering directions and applying nulling

## Slide 21: mmSubArray Enables JointNets
High speed wireless mmWave backhaul – no more expensive fiber backhual.
Ensures Coexistence - suppress interference and support users effectively.
Achieves high spectral efficiency on both networks and avoid coverage gaps.
Ground station
Satellite
Direct to device
Satellite Link
Remote user
User within 5G coverage
High speed wireless
mmWave backhaul
5G Link
5G Base
station
Questions?
Artifacts and more details at
wcsng.ucsd.edu/ mmsubarray

## Slide 22: Additional slides

## Slide 23: Current approaches to address interference: Frequency Separation (Filtering)
Wireless
mmWave backhaul
Ground station
Satellite
Direct to device
Satellite
Uplink (desired)
5G base station coverage area
Remote user
User within 5G coverage
5G Base
station
5G Link
Satellite uplink
Satellite uplink and 5G links are in different frequency bands, discarding overlapping bands and only use non-overlapping bands for 5G links
No coverage gaps
Spectrum wastage
Integrates Satellite and 5G Networks

## Slide 24: Current approaches to address interference: Angle Separation (Beam nulling)
5G Link
Ground station
Direct to device
Satellite
Uplink (desired)
5G base station coverage area
Remote user
User within 5G coverage
5G Base
station
Satellite
Uplink leakage (undesired)
Satellite
5G Base station uses phased array to do beam nulling, this approach suppress all frequencies in nulling direction, thereby by nullifying interference effect.
Coverage gaps
Full spectrum usage
Cannot integrate Satellite and 5G